Creating a Fixture Calibration Executive - Cassini
Fixture Calibration Executives do two things.
Provide an area to list all required calibration plans for a fixture.
Provide an order of succession for required test plans.

---
Steps for Creating1
Open the Device Connection Editor
  - To do this go to the upper right hand corner of the screen and choose
    "Apps" from the screen side menu. An application window will pop up.
  - Select "Device Connection Editor" button and the device editor window will open.
  - Select the “Fixture” tab to load the desired fixture definition.
Fixture Tab
Device Connector
 Editor Window

---
Steps for Creating2
Load the Desired Fixture Definition
  - After choosing the “Fixture” tab, highlight from the listing window the fixture
     that will have the calibration plans listed and select OK at the bottom of the window.
  - After the Device Connection Editor loads,
     choose “Edit Cal List” from the pull down
     menu.

---
Steps for Creating3
Adding Calibration Plans
  - In the “Calibration List” window do a RMBC in the clear area and choose “Add”.
  - Select “Calibrate” for the type of test plan.
  - Select the calibration test plan name from the test plan list.
  - Select “OK” at the bottom of the window when you have added all the test plans.
1
2
4
3

---
Notes
In order to have a Calibration plan listed in the calibration list they must be saved as a calibration plan and the fixture family needs to be selected in the file save process.
Note: in order for verify/validate test
plans to display results the limits
in the test plan need to be named
“Systemcheck”.