The Software Fixture
What does the Software Fixture do?
The software fixture provides to the tester the schematic representation of the
hardware fixture.
It provides the proper RF path definitions to which calibration data can be passed
and saved.
It also provides proper configuration settings for any RF switches or signal processing
modules that may exist in the fixture.
The type of calibration required for each DUT Pin Interface is also defined by the
software fixture.
Proper standard calibration routines for each fixture created can also be defined.

---
Real Time Example
Creating the RF000 Fixture
Initial fixture creation
Defining the path DutRF1/RF3
Editing the path	- Mode	- Switch	- Description
Finish Path Definitions for the schematic – student activity.
[Speaker Notes: Use virtual PC for this and walk through each path with them. Let them come up with the answers to fill in the blanks.]

---
Student DUT/Fixture
Example Path
RF000
Note DutRF
and Resource
Clk
VccPA
Data
M3
Stb
J11
PA out
DutRF1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF3
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP2
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF2
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
DutRF Locations
 DutRFXX = JXX
J3
J5
J1
J20
J2
J6
J4
J19
J7
J18
J8
J17
J9
J16
J14
J10
J12
J15
J11
J13

---
Creating a Software Fixture
1. From the Test Environment window
    select “Test – Fixtures”. A fixture	window will open.
2. From the “Fixtures” window pull down menu select “New - Fixture”.
3. You will then be prompted to “Select a Fixture class”.
     Select the Smart Fixture for 20/25 RF square DUT boards. Name the fixture “RF000” when prompted.
[Speaker Notes: 1. Cover this slide and then review the training fixture schematic on slide 3.]

---
Fixture Path Definition and Editing
1. Highlight the new fixture and use a right mouse button click to get to the fixture
    pull down menu. From this menu choose “Edit”. A fixture edit window will pop up.
Allows fixture
family
To edit Dut Interface
Pins (cable type
fixtures only)
To define
new paths.
To edit paths
To delete high-
lighted paths
Lists completed fixture
path definitions
To save all changes
 To cancel all changes

---
Path Definition Window
2. Choose “Add” to get to the “Path Definition” window.
DutRF1.....DutRFXX
Additional path definition
Scroll to define
Tester
Resource
Module control string
Shows up in
path listing
None
RF
AC
Tuner
Inspect path cal data
To save all changes
 To cancel all changes

---
Path Definition Result DutRF1/RF3

---
Commence Exercise
Finish defining the fixture paths
using the fixture file created in
slide 5.
Example Path
RF000
Note DutRF
and Resource
Clk
VccPA
Data
M3
Stb
J11
PA out
DutRF1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF3
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP2
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF2
RF4
30dB
RF2
J5
J10
J2
90
+

---
Exercise Finished Results