CASSINI RF/ Microwave ATE System
Advanced Test Plan Concepts

---
 Device Centric Testing
 Family Definitions

---
Connection the Device to the ATE
Create a Device Definition
Create a Device Pins Definition
Create a Fixture Definition
Create a Device Interface Board ( DIB )
Create a Protocol Aware Device Control Definition

---
First Create a Device Definitions file

---
Create a Device Pins Definition

---
Create a Test Fixture Definitions file

---
Create a Device Interface Definitions file	DIB or Load Board

---
Create a Protocol Aware Device Control Definition – Serial or Parallel

---
Dut Controlled by Serial or Parallel Port

---
*23
DUT Serial Port
DUT Created
Put in Test Plan

---
DB Lines
Static digital control
Serial bus
Parallel bus
Leakage (low current) measurements
ESD diode check (force current)

---
Serial/Parallel Bus Control
DUT Defined or "Brute Force"
DUT Defined Contained in Dut Instrument
Single Button Programming
Allows Descriptive Names
DUT buttons created

---
DUT Serial/ Parallel Device Control
DUT Created
Put in Test Plan

---
Serial Port Basics

---
Testplan Serial Bus Control
Initial Condition Setup

---
Testplan Serial Bus Control
Initial Condition Setup

---
Serial Port Basics
Fields
16 Bit Bus
Frequency Field
1st Bit: Bit 10
Size: 3 Bits
8 Potential States
0010000100101101
Freq
 1
000
Freq
 2
001
Freq
 3
010
    .
    .
Freq
 8
111
Bit 1
MSB
Bit 16
LSB

---
RI Serial Definitions
Bit order 1 thru N (no bit 0)
Bit 1 is MSB
Bit 1/MSB is on Left
0010000100101101
Bit 1
MSB
Bit 16
LSB

---
Serial Port Basics
Registers
Serial Bus can be Multiplexed into Registers
Bits are Allocated to Register "Address"
Specific Address Changes Field Definition
Allows Expansion of Serial Capability

---
Serial Port Basics
Registers
Address Bits: 15 and 16
Allows 4 Registers
0010000100101111
Bit 16
Bit 1
001000010010111
00
Register 1
0010000100101101
Freq
. Field
Bits 10-12
0010000100101100
Register 0
Atten
. Field
Bits 7-11
01
10

---
Programming Serial Port
Select Serial Type
Dut Defined/Local/I2C/I3C
Assign Static Digital Resources
Clock
Data
Strobe
Define Dut

---
nathan#3
Fast Serial Control
Standard Serial: 60 KB/Second
Fast Serial: Up to 2.5 MB/Second
Fast I2C: Up to 600 KB/Second
Specific Digital Resources
Read: DB 1 or 9, Write: DB 2 or 10
Clock; DB 3 or 11
Must be adjacent

---
*6
Static Digital Resources
Type
Read
Clock
Data
Strobe

---
Static Digital Resources
Assign DB Lines

---
Serial Control
Creating Compound States
Compound States allow High Level Functional Buttons of many Registers
System Rounds Variable Input Data to the Nearest Valid State
Spread Sheet Data Import for Complex or Large Compound State Tables

---
First Create a CSV file with
Serial Data

---
Import the CSV Data into Compound Spread Sheet

---
First Row in CSV are Field Names,
Each Row is a Compound State

---
Editing the Compound Data,
Use Alt & Left Mouse Button

---
Save the Compound Field Data

---
#all above
Sweeping DUT Frequency using Compound Setting

---
DB Lines Description
Switch between Von. Voff, Open
16 lines, 2 banks
4 voltage supplies
1 Precision Multimeter
2 mA limit
+/- 10V

---
Schematic

---
Measuring Leakage Current or ESD Diode Voltage with DB Lines
Select voltage or current measure mode
Set Opposing Limit (V or I Hard Limit)
Set Measure Max. (sets Resolution)
Set DB pin to Open
Select DB pin to be Measured

---
How to Make Low Current Measurements using DB lines
-
+
DB1-8
+
+
+
V
meas
V
V
on
off

---
Leakage Current Measurement

---
Diode Voltage Check

---
Setup The Tester to Meaasure a Device

---
Definitions - Tester Settings
Tester Idle State - Lowest Level Default
Global Defaults - Next Level Default	Test Plan Controlled
Disconnect Settings - Sequence Control	Highest Level Default
Test Plan Idle Settings - Combination of all	Condition Just Before Connect
Connect Sequence - Only Sequence Control	Must put all buttons here in Disconnect!

---
Test Plan Editor Run Time Sequence - Single Run
1
2
3
4
5
6
First
Last
Tester
Testplan
Tester
Testplan
Idle
Idle
Idle
Measure
Idle
Measure
State
Settings
State
Settings
Panel
Panel
Connect Sequence
Disconnect Settings
Disconnect Settings
with First Panel
Delta Settings
Tester Defaults
and Global Defaults
and Global Defaults
Settings

---
Test Plan Editor Run Time Sequence - Repeat/Test Exec
1
2
3
4
5
6
7
First
Last
Tester
Testplan
Tester
Testplan
Idle
Idle
Idle
Measure
Done?
Idle
Measure
Y
State
Settings
State
Settings
Panel
Panel
N
Connect Sequence
Disconnect Settings
Disconnect Settings
Tester Defaults
with First Panel
Delta Settings
and Global Defaults
and Global Defaults
Settings
Connect Sequence
with First Panel
Settings

---
#88
Global Defaults for Source 1, 2 & Settle

---
#99
Global Default Setting for Scr12Output:
Aux + Src2 combined to Src1

---
Disconnect Settings Only

---
Disconnect Settings Panel
Must include all Parameters set by Local Variable in Test Plan

---
Connect Sequence: Left to Right only

---
Averages, One Input Calculations

---
Simple Test at 1 Frequency

---
Using Button 2 Functions

---
Range, Stepped, Tracking, List, Set from LV and Repeat

---
Pause, Pre/Post Measure, Sequence Delay, Samples, Sample Rate, Voltage vs Time & Frequency Count

---
PreMeasure Sequence Left to Right only

---
Sweep Power and Save Data Indexed by Sweep Parameter

---
Changing the Owner of the Button

---
Changing the Owner to Source 1

---
Selecting the Sort by Index

---
Selecting the Parameter Power as the Sort by Index

---
Data Save Button is now Owned by Source 1 & Indexed by Power

---
Calc Only, Local Variable Source, 2 Input Calcs & LV Save

---
Pre Measure, Post Measure, Lockstep & Measure Groups

---
Select and Group Buttons

---
Selecting the Group Function

---
Creates Lockstep Group

---
Lock Step Using CSV File
Spread Sheet Data Import for Complex or Large Lock Step Tables
All Points in the First Column must be Unique

---
Sweeping DUT Frequency using Lock Step with CSV file Data

---
Importing CSV Data into
Lock Step

---
Lock Step with CSV Data
First Row in CSV is Data, not Field Name

---
Editing Lock Step Editor Panel
Click ALT and Left Mouse Button

---
Creating Array Local Variables

---
Array Local Variables Calculations

---
Overview
Tester Viewer Panels
Device Control
Advanced Test Plan Buttons
Generic GPIB Instruments

---
Generic GPIB Instruments
Creating a new GPIB instrument
Configuring GPIB instrument
Using the Instrument in the testplan

---
Creating GPIB instrument
From the RI System message window, use menu Test --> Instruments
From the Instruments Window, use menu Instrument --> Add Instrument
Select "GPIB Instrument"
Enter the Title of the new instrument
Enter the Name of new instrument
Enter the GPIB Address
[Speaker Notes: Title is the filename reference on the disk Name is the instrument name of the button use in the testplan]

---
Configuring GPIB instrument
Activate the GPIB instrument then Startup the tester
Configure the active tester and select the GPIB instrument
GPIB address
Startup GPIB command string

---
Click here to type page title

---
Using GPIB Instrument in the testplan
State button
Initialize
Write, Write 2, Write 3, Write 4
Read Size
Read Command
Measure Button
MEAS Read String
MEAS Read Number

---
Click here to type page title

---
Click here to type page title

---
Overview
Tester Viewer Panels
Device Control
Advanced Test Plan Buttons
Generic GPIB Instruments
Questions?

---
Testset Block Diagram

---
Testhead & Testset Editor

---
Port Set-up

---
Stimulus

---
Receive

---
Sampled Waves