Why Modules?
 Resource Customization, Extension, and Enhancement
RF, AC, DC Switching
Signal Attenuation
Filtering
Differential I/Q Signals and Offsets
Frequency Division
Voltage Buffering
Etc....
Standard Modules Available From Roos Instruments
http://roos.com/docs/JLUT-64A253?Open

---
Module Types
Module Types Based on Levels of Complexity and Control
Level 1 - Require simple static digital control lines.
OTC attenuators, switches, etc... requiring 1 - 8 Cbits
RI developed modules requiring 1 - 4 static control lines
Level 2 - Require more than simple static digital control but do not
        require fixture instrument buttons.
RI developed modules requiring more than 4 static control lines
Only one state or variable to control
Level 3 - Require fixture instrument buttons for control.
More that one variable to be controlled – ie. state and level commands together

---
Level 1 Cbit Control Carrier 65A
Cbit Use:
1. For driving attenuators, switches, relays, and other devices not configured for module slots.
2. Format: “C-#-state” is typed into the switch field of the Fixture File Editor (7100) or the
    Fixture Definition (Cassini).
EX. To switch Cbit2 high type C21 into fixture file switch field.
Cbits
[Speaker Notes: Cbit Use: 1. Used to drive relays, attenuators, or other items not configured for module slots. 2. Control is of the form “C-#-state”. For example, to drive Cbit 2 high, one would type C21 into the switch field of the fixture file editor.]

---
        Level 1 Module Control
        Carrier Module
       Module Control String
1. Control provided through DS1 - DS4.
2. Format: “S# - state-state-state-state”.	# = module position
Example: To drive the lines DS1 and DS3 high at module location M2 type S21X1X into the fixture file switch field.
Carrier “M” location denotes position
        M = S#
From Carrier
Module Control
Note:
1. DS1-4 are not available on Passive carrier boards

---
Level 1 Module Control Exercise
Write the code string required to place Cbit 3 high and Cbit 5 low. In the same
string drive DS1,2, and 4 of the module at M3 high.
Where would the code string be typed?

---
Answer to Level 1 Control Exercise
1. C31C50S311X1 or
    C50C31S311X1 or
    S311X1C31C50
2. In the fixture file switch field.
Note that strings are not delineated and can be mixed.

---
Module Types
Module Types Based on Levels of Complexity and Control
Level 1 - Require simple static digital control lines.
OTC attenuators, switches, etc... requiring 1 - 8 Cbits
RI developed modules requiring 1 - 4 static control lines
Level 2 - Require more than simple static digital control but do not require fixture instrument buttons.
RI developed modules requiring more than 4 static control lines
Only one state or variable to control
Level 3 - Require fixture instrument buttons for control.
More that one variable to be controlled – ie. state and level commands together

---
        Level 2 Module Control
        Carrier Module
       Module Control String
1. Control provided through DS1 - DS4,	DWRT, DRD, and DCLK.
2. Carrier configuration step “Add Module”	required in 7100. “Edit Modules” is used in
   the Fixture Definition on the Cassini.
3. No fixture control buttons required in test	plan.
4. Format: “A#SW=XX” or “A#CX=Y”.	A# = module position	SW=XX or CX=Y is module specific but	still loaded into fixture switch field.
Carrier “M” location denotes position
        M = A#
DCLK
DWRT
DRD
From Carrier
Module Control
Note:
1. DS1-4 are not available on Passive carrier boards

---
Module Types
Module Types Based on Levels of Complexity and Control
Level 1 - Require simple static digital control lines.
OTC attenuators, switches, etc... requiring 1 - 8 Cbits
RI developed modules requiring 1 - 4 static control lines
Level 2 - Require more than simple static digital control but do not require fixture instrument buttons.
RI developed modules requiring more than 4 static control lines
Only one state or variable to control
Level 3 - Require fixture instrument buttons for control.
More that one variable to be controlled – ie. state and level commands together

---
        Level 3 Module Control
        Carrier Module
       Module Control
1. Control provided through DS1 - DS4,	DWRT, DRD, and DCLK.
2. Carrier configuration steps “Add Module” and “Add Instrument” required. This is done in
    the Fixture File Editor on the 7100 and in
    the Fixture Definition on the Cassini.
3. Fixture control buttons are required in test	plan.
        EX.
Carrier “M” location denotes position
DCLK
DWRT
DRD
From Carrier
Module Control
Note:
1. DS1-4 are not available on Passive carrier boards