The Software Device Interface
What does the Software Device Interface do?
The software fixture provides to the tester the schematic representation of the
hardware DIB.
It provides the proper RF path definitions to which calibration data can be passed
and saved.
The type of calibration required for each DUT Pin Interface is also defined by the
device interface.
Proper standard calibration routines for each DIB created can also be defined.

---
Fixture Calibration
Socket
DUT Interface Board (DIB)
Top Plate Assembly
Top Plate & Carrier Board
Modules
Modules
Calibrate to here and
calibrate DIB separately
Calibrate fixture to here
and treat as a single cal
OR
Bottom Plate Assembly
Power VIs
RF
AC
GND
DC
Test Head

---
Initial DUT Creation
1. Got to main environment window
    and pull down the “Test” menu.
2. Choose “Device Interfaces”.
3. Select “New” from the Device
    Interfaces window.

---
Creating Software DUT Interface
4. A fixture type selection box will open.
    Select type = Smart Fixture for 20/25
    RF Square Dut Boards.
5. Name the new Device Interface
    “Student_RF000” and select “OK”.

---
Creating Software DUT Interface
6. A selection window will appear. Select “all duts.
7. A new Device Interface will appear in the Device Interfaces window.

---
Editing the Device Interface
1. If a DUT was created, make sure it is activated.
2. Highlight the Device Interface to be editied and with a RMBC select “Edit”. An edit window will appear.

---
Editing the DUT Interface
DutP 1-272 and
DutRF 1-30
Will reflect DUT pin names
as defined in DUT.
Inspect
Calibration

---
Assign DUT pin
to tester resource

---
Assign
calibration
type

---
Student RF000 Device Interface