Fixture Functional Block Diagram
What is Required?
1. DUT pin outs: DUT Functional Block Diagram
2. DUT pin resource requirements - RF, AC, DC, or Digital:
    DIB Schematic
3. External Circuitry required for each DUT pin:
    Fixture Schematic
4. Tester, handler, and socket implementation

---
Creating the Fixture Schematic
Three Major Steps
1. DUT Functional Block Diagram
2. DIB Schematic
3. Fixture Schematic

---
DUT Functional Block Diagram
Also which device pin# is it
Step 1: What is it and
what does it require
DUT
RF000
P2
DC Source and Measure
Clk
P28
VccPA
Digital Source
Data
P27
P4
Stb
P26
PA out
P24
RF Source
RF Measure
PA in
P22
P6
Q in
AC Source (WF)
Mod out
P20
RF Measure
+
90
P8
I in
P18
DModin
RF Source and Measure
RF Source (LO)
P10
I out
AC Measure Phase
and Amplitude (WF)
P12
I/Q Modulator
I Q out
P14
RF Source (LO)
P16
I/Q Demodulator
90
+

---
Device Pin Names and Numbers

---
Creating the Fixture Schematic
Three Major Steps
1. DUT Functional Block Diagram
2. DIB Schematic
3. Fixture Schematic

---
Student DIB Block Diagram
Step 2
Step 2: Identify board components
(ie. caps, resistors, etc...) and
edge connections.
DutP# = Pogo#
RF000
Clk
VccPA
DutP30,31,&32
Data
DutP25&26
Stb
PA out
DutRF1
PA in
DutRF4
Q in
DutP2
Mod out
DutRF5
+
90
DutRF2
I in
DModin
DutRF6
DutP1
I out
DutP3
I Q out
DutP4
DutRF3
90
+

---
Student Fixture Block Diagram
Step 3
DutP# = Pogo#
Step 3: Identify Tester Resources
RF000
DP1
Clk
VccPA
DutP30,31,&32
DutP25&26
Data
Stb
PA out
FHSD
DutRF1
PA in
DutRF4
RF3
Q in
DutP2
RF6
Mod out
DutRF5
+
90
WF2
DutRF2
I in
DModin
DutRF6
RF7
DutP1
WF6 & RF4
I out
DutP3
WF3
WF7 & RF4
I Q out
DutP4
RF2
DutRF3
90
+

---
DIB Schematic Creation
Fixture Top Assembly.
Device Interface Board I/Os.
Fixture Carrier Board
  - Type (Smart vs Passive)
  - Single-site, Dual-site, or Multi-site.
Socket Type required for the DUT.
DUT to DIB resource route names

---
Creating the Fixture Schematic
Three Major Steps
1. DUT Functional Block Diagram
2. DIB Schematic
3. Fixture Schematic

---
Student Fixture Block Diagram
Step 4
Step 4: Identify fixture
components and Modules
Fixture High
Speed Dig
RF000
Clk
VccPA
Data
M9
Stb
PA out
J11
M1
DutRF1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF2
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP4
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF3
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
The Spreadsheet
Why A Spread Sheet?
Textually describes the fixture assembly for repeat builds.
Major Sections:
1. General information
2. Assembly notes
3. RF path descriptions
4. Module locations
5. Specific non pogo pin connections
Module to Module
 Resource to Module
 Resource to DutRF
 6. Pogo pin connections

---
Spreadsheet – General Info

---
Spreadsheet - Assembly Notes
Notes:
1) Bottom Plate: Pin 32 of header 1 needs	clipped for compatibility with old test systems.
2) Resource Number is for factory internal use.
3) Documentation to be included:
* Smart Carrier Module Truth Tables.
* Smart Carrier Control Bit Programming.
* Software Fixture
4) Baluns for DIB provided by customer.

---
Spreadsheet - RF Paths
RF Routing and Control:

---
Spreadsheet - RF000 RF Paths
RF Routing and Control:
To be filled out in class

---
Student Fixture Block Diagram
Record pin name as well
Fixture High
Speed Dig
RF000
Clk
VccPA
Data
M9
Stb
PA out
J11
DutRF1
M1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
Take each RF/AC path and record
its DIB pin and attached resource.
Can also include control strings.
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF2
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP4
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF3
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
Spreadsheet - RF/AC Paths
RF000
RF Routing and Control:
All level 1 control
Note: Modules are in positions 9 & 10

---
Student Fixture Block Diagram
Record each module type and locations.
Fixture High
Speed Dig
RF000
Clk
VccPA
Data
M9
Stb
PA out
J11
M1
DutRF1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF2
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP4
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF3
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
Spreadsheet – Module Locations
RF000
Module and Instrument Locations

---
Student Fixture Block Diagram
Record pin name as well
Fixture High
Speed Dig
RF000
Clk
VccPA
Data
M9
Stb
PA out
J11
DutRF1
M1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
Take each RF/AC path and record
its DIB pin and attached resource.
Should also include control strings.
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF2
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP4
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF3
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
Other Connections
Non-Pogo AC/DC and Specific RF Connections:

---
Student Fixture Block Diagram
Record specific resource and
cable type to each node in path.
Fixture High
Speed Dig
RF000
Clk
VccPA
Data
M9
Stb
PA out
J11
M1
DutRF1
RF3
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP2
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
Example Path
WF3
I in
DutRF6
DModin
MA(10)
DutRF2
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
Example Path
I Q out
J16
J5
WF7
50
J12
DutP4
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF3
RF4
30dB
RF2
J5
J10
J2
Example Path
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
Spreadsheet – Non Pogo Connections
Non-Pogo AC/DC and Specific RF Connections:
Example paths

---
Student Fixture Block Diagram
Take each DC/Dig and record
its attached resource.
Can also include control strings.
Fixture High
Speed Dig
RF000
DutP10
Clk
DutP20
VccPA
Data
DutP21
M9
Stb
DutP22
J11
PA out
DutRF1
RF3
M1
J4
30dB
RF6
PA in
DutRF4
J5
J6
DutP4
J12
Q in
WF2
DutRF5
Mod out
+
90
DutP1
WF3
I in
DutRF6
DModin
MA(10)
DutRF3
RF7
WF6
DutP3
J10
50
J3
Mod LO in
I out
J1
I Q out
J16
J5
WF7
50
J12
DutP2
MA(10)
M9
J9
J1
J1
DMod LO in
DutRF2
RF4
30dB
RF2
J5
J10
J2
90
+
[Speaker Notes: 1. Have them note the DutRF1/RF3 path on slide 3. This will path will be defined real time as an example using the virtual PC existing on the computer. The RF000 fixture will be created at this time. 2. Review slides 4,5 and 6 before going into the real time fixture creation and definition of DutRF1/RF3 path.]

---
Spreadsheet - Pogo
Connections
Pogo Resource Allocation and Notes: